MicroPython Basis

# Download and install MicroPython

Download the latest version of micropython for the esp32 from https://micropython.org/download/esp32/
Look for Firmware built with ESP-IDF v3.x, with support for BLE, LAN and PPP and SPIRam
At the time of writing we use:
“esp32spiram-idf3-20191220-v1.12.bin”

I use com port com7 in this document

esptool.py --chip esp32 --port com7 erase_flash

esptool.py --chip esp32 --port com7 --baud 460800 write_flash -z 0x1000
esp32spiram-idf3-20191220-v1.12.bin

# Download and install a display driver

for this tutorials, I used modified files from the github page …
Download all files from this repository to your computer.
According to your needs, upload the images folder to the esp32’s images folder and the fonts to the fonts folder.
upload the python files to the root of the ttgo board
upload the ‘images’ folder to the ‘images’ folder of the ttgo
upload the ‘fonts’ folder to the ‘fonts’ folder of the ttgo
note that not all files can be stored to the ttgo at the same time, just copy the files needed for a specific project.

In almost all projects, I use the create_display() function from display.py to create a display. By using this function, it will be easy to move to another display driver. The function create_display() looks like this.

"""
display routines
"""
# test of printing multiple fonts to the ILI9341 on an M5Stack using H/W SP
# MIT License; Copyright (c) 2017 Jeffrey N. Magee
# Adapted for Sensemakers. Changed pins for the TTGO T4-V1.3 board

from ili934xnew import ILI9341
from machine import Pin, SPI, PWM

bg_led = None

def create_display(rotation=0):
    """
    Create a connection with the display
    """

    global bg_led
    bg_led = PWM(Pin(4))
    bg_led.freq(1000)
    bg_led.duty(750)

    spi = SPI(2, baudrate=30000000, miso=Pin(12), mosi=Pin(23), sck=Pin(18))
    display =
ILI9341(spi, cs=Pin(27), dc=Pin(32),
        rst=Pin(5), w=320, h=240, r=rotation)

    display.erase()
    display.set_pos(0, 0)

    return display

# Show I2C addresses
Needed files:
- Ili934xnew.py
- Display.py
- Fonts/roboto_cond_reg_12.py
- Fonts/roboto_cond_reg_18.py
Final project file:
I2cscanner.py

Create a new python file named i2cscanner.py

…